## Slide 1: Year 1 Software Training
2023

## Slide 2: Introductions
Name
Students: Year in School / Mentors: job experience
Coding Experience
Robotics Experience
Favorite Movie / TV Show

## Slide 3: Getting Started
Laptop with admin privileges
  Personal
  Team laptop
  Cannot be school laptop
  We’ll use team laptops tonight

## Slide 4: Training
Cover topics – multiple times with hands on examples
Questions – ask when something isn’t clear
Material will be posted online in Teams on the Software Channel
Leverage WPI/CTRE/REV documentation
  https://docs.wpilib.org
  https://docs.ctre-phoenix.com/en/stable/
  https://docs.revrobotics.com/sparkmax/software-resources/spark-max-api-information

## Slide 5: Goals
Learn FRC Coding environment & the tools we use
Learn how to code FRC robots the 302 way
Write Code to support Y1 Connect 4 Robot
Add something to the Team 302 Base Template
Get Prepared for FRC Varsity Season
Do some 2023 FRC WPILIB beta testing with our base code

## Slide 6: Frc Environment - Tools
WPI Tools
VS Code
GitHub/GitKraken
PathWeaver
System Identification
RoboRio Imaging Tool
Radio Configuration Tool
Robot Simulator
Dashboards
Shuffleboard
SmartDashboard
LabView Dashboard
Glass
LiveWindow
Custom
Vendor Tools
Phoenix Tuner
REV Hardware Client
Limelight Finder
Notes: High-level overview – show at docs.wpilib.org

## Slide 7: Activity
Get Laptop
Follow along
  RoboRio Imaging Tool
  FRC Radio Configuration Tool
  Phoenix Tuner

## Slide 8: Frc Environment - Coding
Languages
JAVA
C++
LabView
Python
Methods
Command Based
Timed Robot
RobotBase Skeleton
RobotBuilder

## Slide 9: Activity
Get Laptop
Follow on screen to create a C++ project using VS Code

## Slide 10: Header / Implementation Files
Could be one file, but is normally separated
Header (.h) file
  Contains Class Definition
  Allows other classes to “include” these so they can call this classes methods
Implementation (.cpp) files have the logic that is executed*

## Slide 11: Header File – Review Robot.h
#pragma
#include
Class definition and hierarchy
Visibility (public, private, protected)
  Methods
  Attributes

## Slide 12: implementation File – Review Robot.cpp
#include
Methods defined in header file implemented
Review when standard robot methods (e.g. when called and timing)
Common includes: string, iostream
Standard variable types
Variable scope
Calling provided methods

## Slide 13: Activity
Add Counter to Robot code to see how many times things were hit using COUT

## Slide 14: Introductions
Name
Favorite Video Game, Board Game or Card Game
Questions from last time

## Slide 15: Review
RoboRio Imaging Tool
Radio Configuration Tool
Phoenix Tuner Overview
VS Code
  Created Project
  Wrote Code to count how many times in each main method and wrote output to the console

## Slide 16: Objects vs. Classes
Class is the “recipe” or “blueprint” for object
  Subclasses are more specialized recipes
Object is an instance of a Class
1 class can have many objects created from it
So, a Wheel class could instantiate a left front wheel, right front wheel, left back wheel and right back wheel.

## Slide 17: Class/subclass/object
(base) class: Dog
(sub) class: Golden Retriever
(sub) class: Dalmatian
Objects of class Golden Retriever: B-Dawg, Buddha, Budderball, Mudbud, Rosebud, etc.
Objects of class Dalmatian: Pongo, Perdita, Patch, etc.

## Slide 18: Activity
Class or Object
Willis (aka Sears) Tower
Golden Gate Bridge
Fenway Park
Skyscrapers
Mackinac Bridge
Wembley Stadium
Bridges
Empire State Building
Wrigley Field
Brooklyn Bridge
Transamerica Pyramid
Stadiums
Lambeau Field
Petronas Towers

## Slide 19: Activity - Answers
Class or Object
Willis (aka Sears) Tower - object
Golden Gate Bridge - object
Fenway Park - object
Skyscrapers - class
Mackinac Bridge - object
Wembley Stadium - object
Bridges - class
Empire State Building - object
Wrigley Field - object
Brooklyn Bridge - object
Transamerica Pyramid - object
Stadiums - class
Lambeau Field - object
Petronas Towers - object

## Slide 20: Activity
Class or Object
Marvel Super Hero
Black Widow
Green Lantern
Superman
Hulk
Aquaman
Iron Man
DC Comic Super Hero
Captain America
Super Hero
Wonder Woman
Black Panther
Batman

## Slide 21: Activity - answers
Class or Object
Marvel Super Hero - class
Black Widow - object
Green Lantern - object
Superman - object
Hulk - object
Aquaman - object
Iron Man- object
DC Comic Super Hero - class
Captain America - object
Super Hero - class
Wonder Woman - object
Black Panther - object
Batman - object

## Slide 22: Creating an object
Constructor – method name matches class name + no return type
new, make_shared, make_unique
Singleton

## Slide 23: WPI Classes
Static Methods vs. Non-Static Methods
Read Method signatures (review with WPI classes)
  NetworkTable
  SmartDashboard
  Timer

## Slide 24: Activity
Using the static methods from SmartDashboard to replace cout calls for the counters

## Slide 25: Activity
Create 3 Timers to keep track of:
  Overall time since the robot was turned on
  Time in Auton
  Time in Teleop
Write the output values in a SmartDashboard

## Slide 26: Introductions
Name
What’s your favorite kind of ice cream?
What’s your favorite Halloween Costume that have you worn?
Questions

## Slide 27: Review
RoboRio Imaging Tool, Radio Configuration Tool, Phoenix Tuner
VS Code – Create Project/Write Code/Build Code
Code
  Count how many time main methods are called send to console then SmartDashboard
  Replace Counters with Timers
Classes vs. Objects – instantiate classes

## Slide 28: CTRE WPI_TalonSRX
https://docs.ctre-phoenix.com/en/stable/
Add a WPI_TalonSRX to our robot project and make it spin in auton

## Slide 29: Activity
Make the motor reverse direction every 10 seconds

## Slide 30: Reading Encoders
https://docs.ctre-phoenix.com/en/stable/
Delete the timer and counter stuff from our project
Read encoders during auton and put them up on the SmartDashboard

## Slide 31: Activity
Update Auton to spin the motor for 1000 encoder counts and then stop the motor

## Slide 32: XBOXController
https://docs.wpilib.org/
Add an XboxController to our project

## Slide 33: Activity
Make the motor spin in Teleop
Make motor spin in teleop with joystick control

## Slide 34: Activity
Get Access to GitHub by sending email to joe.witcpalek@gmail.com with subject of GitHub
Complete follow up steps when you are invited

## Slide 35: Base Library Review
XML Robot Definition
XML Parsing
Mechanism Base Classes
Mechanism States

## Slide 36: Activity
Year 1 Robot Review
  Identify Mechanisms and what will their Base Class should they inherit from

## Slide 37: Activity
Complete your GitHub invitation
Make sure laptop is updated to beta environment
Sign out an issue on the project and drag it into the In Progress Column
Create a branch for your work
Use GitKraken to clone Repository
Open VS Code to work on your item
Commit changes when it compiles
Push up to Github and create a pull request

## Slide 38: States Review
Review States

## Slide 39: Activity
Year 1 Robot Review
  What states will each Mechanism have

## Slide 40: Activity
Access Year 1 project in GitKraken
Create a branch – your name

## Slide 41: Add A chassis Class
Create a Chassis class
Inside the Chassis Class, hold onto:
  frc::MecanumDrive object
  a Pigeon (note difference between PigeonIMU and Pigeon2)
  frc::MecanumDriveKinematics object
  frc:: MecanumDriveOdometry object
Provide public methods to drive the chassis, return its position and update odometry
Create an instance of Chassis in RobotInit
Update the odometry in RobotPeriodic

## Slide 42: Activity
Add a method to reset the chassis’ position to a known position
In AutonInit, reset the robot’s position to 0 meters, 0 meters and its angle to be 0_degrees
Make Auton drive the chassis forward
Report its current pose in AutonPeriodic to a NetworkTable